CESAR -Channel Estimation- Architecture / Preliminary version A1 14/03/08

CESAR -Channel Estimation- Prototype
Architecture

This document describes the architecture of the 'Channel Estimation' process for Cesar firmware

Revision	Date	Author	Comments
A1	10/03/08	JL

References
[Ref1]	Homeplug AV Specification :
file://Gevrey/spidcom/tek/Projets/04-319__HOMEPLUG_AV/Project_Management/HomePlug%20AV%20Specification%20v1.1.pdf

[Ref2]	'bit loading' documentation :
...
Acronyms
CE	: Channel Estimation
MAC	: Medium Access Control
PB	: PHY Block
CP	: Control Plane
PHY	: Physical layer device
PLC	: Power Line Communications
DSP	: Hardware processing.
MME	: Management Message Entry
FC	: Frame control
TXCE	: CE for transmitted data.
RXCE	: CE for received data.
CEI	: CE indication (MME)
SCF	: Sound Complete flag.
SRC	: Sound Reason Code.
TMI	: Index of tonemap.
TEI	: Terminal Equipment Identifier.
STEI/DTEI : Source/Destination TEI.
AVLN : Network HPAV.

## Introduction
### CESAR environment
#### Memory block.
lib/blk.h
All the dynamically allocated memory is fragmented with 512-bytes data block plus 4-bytes as reference counter and 16-bytes as descriptor. The first word of the descriptor point eventually to a next block, the second point to data.

struct blk_t
{
/** Pointer to next descriptor. */
struct blk_t *next;
/** Pointer to data. */
u8 *data;
};
#### Tonemap.
mac/common/tonemap.h
A tonemap is made of up two blocks (2 descriptors a,d 1024 bytes of data). The first descriptor points to the last. The (512+256)-first data can describe 1536 modulations. (1 byte for 2 modulations). The following 256 bytes data allow to store additionnal information about this tonemap; In particular, it is stored a pointer to the first descriptor. So, the software can read all information of the tonemap and can give the address of the first descriptor to the hardware. Thanks to this address, the hardware can read the list of modulation.
Note : The first carrier is the first usable carrier. (In HOMEPLUGAV mode, this is the 74th carrier among the 1536 of the FFT.)
tonemap_t
{
....
blk_t *tmdma_desc_head // Point to the first descriptor.
....
}

#### Set of tonemap.
mac/common/tonemap.h
It is called a 'tonemaps', a set of tonemap with, in addition, a set of interval, and any common parameter of the set.
mac/common/tonemap.h
tonemaps_t
{
...
cyg_count_t expiration_rtc_date
tonemap_t *tm[MAX_TONEMAP];
...
}
For more details about interval and tonemaps, see “bitloading” documentation.
All this data is necessary for DSP and PBPROC to encode and decode the frames. In addition, it is store a date information. For transmission, it allows to store the expiration date , updated each time a CEI is received concerning this set of tonemap. (new_date = current_date + 30 seconds). For reception, it allows to store the refresh date from which the process will have to create a CEI.

#### Remote station.
mac/common/sta.h
The sta_t structure allows to store information about a remote station. For the CE, it allows to find the both set of tonemap. One used for transmission with the remote station, the other for the reception a frame coming from the remote station. There are called respectively 'tx_tonemaps' and 'rx_tonemaps'. The 'tx_tonemaps' is created from received CEI. The 'rx_tonemaps' are created for computed measures done on remote station received frames. The 'rx_tonemaps' are transmitted to the remote station thanks to the CEI.

sta_t
{
...
tonemaps_t *rx_tonemaps
tonemaps_t *tx_tonemaps
}

#### Mac_store.
mac/common/store.h
The mac_store allows to manage and store data about all remote stations of the AVLN. Each station have a personnal TEI. API functions as 'mac_store_sta_get (uint tei)' allows to get a pointer to the corresponding sta_t structure and so the set of tonemaps.

The mac_store for Channel Estimation :

mac_store

sta_t[TEI]
{
    ____
    tonemaps_t *rx_tonemaps
    tonemaps_t *tx_tonemaps
    ____
}

tonemaps_t
{
    ____
    ____
    tonemap_t *tm[N];
    ____
    ____
}
desc
1024
carriers

desc
512 carriers

tonemap_t
{
    ____
    blk_t *f
    ____
}

### CEI.
ce/inc/cei.h
A CEI is a message sent by a station to another. When a CEI is received by the station, it decodes it in order to update its set of tonemaps used to transmit to the source of CEI station.

#### Message CEI structure.
3 types of CEI exists :

- CM_CHAN_EST.IND with modulations coded carrier by carrier (non-masked). (absolute)
- CM_CHAN_EST.IND with modulation coded by group of consecutive with the same modulation carriers.(absolute and compressed)
- CM_UPDATE_TM.IND describes the differences between the new tonemap and an existing one (relative).
MME / HEADER	ODA	48
	OSA	48
	[VLAN Tag]	32
	MTYPE constant : 0x88E1	16
	MMV	8
	MMTYPE 0x6014(cm_chan_est.ind) or 0x6018(cm_update_tm.ind)	16
	FMI (in CEI case, FMI = 0)	16
MM_ENTRY / OF / CEI	MAX_FL_AV	16
	RIFS_AV_OneSym	8
	RIFS_AV_TwoSym	8
	RIFS_AV_G2Sym	8
	RESPT	8
	MAX_TM	8
	CP_TMI_AV	8
	SCL_CP	8
	SCL_CFP	8
	VALID_TM_LIST / L (nb entries) 8 / TMI[0] 8 / ... / TMI[L-1] 8	8+L*8
	INTERVAL_LIST / M (nb entries) 8 / { ET[0] TMI[0] } 16 + 8 / ... / { ET[M-1] TMI[M-1] } 16 + 8	8+ M*(16+8)
	OLD_TMI	8
	NEW_TM / NEW_TMI_AV 8 / CPF 8 / FECTYPE 8 / GIL 8 / DATA / Case Absolute Case Absolute and compressed Case Relative / CBD_ENC 8 / N1 16 / CBD[0] 4 / ... / CBD[N1-1] 4 CBD_ENC 8 / N2 16 / CBD[0] 4 / ... / CBD[N2-1] 4 N3 16 / CBD[0] 16 / ... / CBD[N3-1] 16 8+16+N1*4 / or / 8+16+N2*4 / or / 16+ / N3*4	8*6+ / (8+N1*4) / or / (8+N2*4) / or / (N3*4)
	PAD	0 or 4

#### Choice among CEIs.
Choose between 'absolute case' and 'compressed absolute case' :
The compression (Run Length Encoding) is always used.
Following table describes the codes used for the compression. The range (on the right) shows the number of consecutive non-masked carriers with the same modulations. On the left, there are the corresponding codes.

      0, 0, 0,	// 00 - 02
      0x8, 0x9, 0xA, 0xB, 0xC, 0xD, 0xE, 0xF,	// 03 - 10
      0x88,0x89,0x8A,0x8B,0x8C,0x8D,0x8E,0x8F,	// 11 - 18
      0x98,0x99,0x9A,0x9B,0x9C,0x9D,0x9E,0x9F,	// 19 - 26
      0xA8,0xA9,0xAA,0xAB,0xAC,0xAD,0xAE,0xAF,	// 27 - 34
      0xB8,0xB9,0xBA,0xBB,0xBC,0xBD,0xBE,0xBF,	// 35 - 42
      0xC8,0xC9,0xCA,0xCB,0xCC,0xCD,0xCE,0xCF,	// 43 - 50
      0xD8,0xD9,0xDA,0xDB,0xDC,0xDD,0xDE,0xDF,	// 51 - 58
      0xE8,0xE9,0xEA,0xEB,0xEC,0xED,0xEE,0xEF,	// 59 - 66
      0xF8,0xF9,0xFA,0xFB,0xFC,0xFD,0xFE,0xFF	// 67 – 74

The nibbles must be written as following :
Hence n, the number of consecutive with same modulation m non-masked.
Hence N or N1N2, the code of n. (table above).
Hence M, the code of the modulation m. (Between 0 and 7 for modulation between NONE to QAM1024.)
If n=1	add nibble 'M' in the buffer.
If n=2	add both nibbles 'M,M' in the buffer.
If 3 <= n <= 10 add both nibbles 'M, N' in the buffer.
If 11 <= n <=74 add the 3 nibbles 'M,N1,N2' in the buffer

The algorithm make a computation instead of an access to a table :
If 3 <= n <= 10 write bith nibbles : 'M, (n-3)|8'
If 11 <= n <= 74 write the 3 nibbles : 'M, (n-3)>>3+7, (n-3)|8'
For the decompression, the separation between a modulation nibble or a run length encoded nibble is done thanks to the fact that M is always down 8 and N is always above 7.

Choose between 'compressed absolute case' and 'relative case' :
The Standard requires that the shortest message must be transmitted. The both type of message should be computed and compared. It seems too long. However, while the 'bit loading' computation, the algorithm knows if it has improved an existing tonemap or created a new one. We can suppose that if it improves an existing one, a few carriers are changed and so a CM_UPDATE_TM.IND should be used.
Moreover, only non-masked carriers are described in the CEI. So functions to create and decode CEI must know the tonemask. (In the tonemap, all the usable carriers are stored.)

#### CEI Creation.
ce/inc/cei.h
The header consists in common fields of all the MME. CP handles it. (cf. Storage of a CEI param.) However, CP need to know the chosen MMTYPE, and the message length.
cei_created_status_t { uint length; uint mm_type;}
Next part of CEI is the MM_ENTRY. The CP provides a destination buffer for the CE in providing a pointer to the start of the MM_ENTRY. In order to fill all the fields of the MM_ENTRY, it is necessary to know :
- the set of tonemap that must be described.
- eventually, the index of the new tonemap
- eventually the index of an existing tonemap if it has been used to create the new one.

Hence the following function for CEI creation :
cei_created_status_t
cei_create (u8 *mm_entry, u8 *mask, tonemaps_t *rx_tonemaps,
uint new_tmi, uint old_tmi)

This function use the 'bitstream' library in order to write nibbles and others fields as expected by the Standard. Data are always compressed following the algorithm above. It returns the MM_ENTRY length and its type determined by the old_tmi value. (If old_tmi = TONEMAP_INDEX_NULL, then the message is a CM_CHAN_EST.IND else a CM_UPDATE_TM.IND.)
All necessary data to create CEI is available in the set of tonemap. (rx_tonemaps)

#### CEI Decoding.
ce/inc/cei.h
The CEI decoding part is the reciprocal of its creation. It use the 'bitstream' library as read and update the set of tonemaps (tx_tonemaps) concerned. The knowledge of the CEI type and the MM_ENTRY address is already done by the CP when decoding the MME header. Moreover, the function need to know the tonemask if a tonemap is described in the message.

void cei_decode (tonemaps_t *tx_tonemaps_to_update, int mm_type, u8 *mm_entry, u8 *mask)
Finally, when a set of tonemaps (tx_tonemaps) is updated by a CEI message made from a set of tonemaps (rx_tonemaps), then both sets must be identical. Or more precisely, all the tonemaps existing in tx_tonemaps shall be identical with those of the rx_tonemaps with the same index. The intervals and others parameters must be equals.

### The Sound MPDU.
The Sound MPDU are frames with known-by-receiver data. So, the several measures done by DSP on data are more confident. Those frames are sent for several reason described in 'http://pessac/cesar/trac/wiki/SoftMacPbproc/Tonemaps'. Then, the FC contains a 'Sound Reason Code' (SRC) allowing to manage the behaviour of the Channel Estimation. (cf. Sound Complete Flag estimation)

## Goal of Channel Estimation.
'Channel Estimation' (CE) is a module allowing to manage the creation, the update, and the elimination of the sets of tonemaps exchanged between each stations of a same AVLN. A tonemap is (mainly) a list of modulation for all the usable carriers.
The management of these tonemaps allows :
- At reception of an MPDU, to know the modulations used when coded and so can be decoded.
- At transmission of an MPDU, to use the best possible modulations.
Two stations communicating together exchange a set of tonemaps. All the tonemaps are referenced by their index. At reception, the tonemap used can be found thanks to the knowledge of the emitting station (STEI) and the index of this tonemap (TMI_AV). This information is transmit in the FC coded with known and fixed modulations.
Note : The TEI is a unique identifier number of a station in an AVLN.

In CESAR project, the 'mac_store' of a station is responsible to store data relative to other known stations. In particular, the Channel Estimation is interested in the set of tonemaps.
The RXCE is the part of the CE responsible of managing tonemaps used for the reception of MPDU. (rx_tonemaps). The TXCE is the part of CE that manages the tonemaps used to transmit MPDU.(tx_tonemaps). When a new station is detected and stored in the mac_store, the memory necessary to store the sets of tonemaps is allocated. (but not the tonemaps)
To explain more clearly, here is the sequence of channel estimation when two stations want to exchange data (in one direction).
Hence rx_sta and tx_sta, with respective teis, rx_tei and tx_tei.
In the tx_sta 'mac_store' is known the rx_sta, with a set of tonemaps, the tx_tonemaps available by the function mac_store_sta_get(tei_rx) .
In the sa me way, in the rx_sta 'mac_store', it is known the tx_sta and so provides a access to the set of tonemaps rx_tonemaps.
For a transmission to a destination rx_sta MPDU, the low layer (PBPROC) of the tx_sta will choose a tonemap among the set of tonemaps corresponding to the rx_sta. The chosen tonemap is referenced by its tmi_av and is indicated in the FC of the MPDU. At reception, the rx_sta is extracting the tx_tei, and the tmi_av from the FC . Then it obtains the tonemap used from the mac_store :
mac_store_sta_get(tx_tei)->rx_tonemaps->tm[tmi_av].

So that it works, it is necessary that tonemap data pointed by :
mac_store_sta_get(tx_tei)->rx_tonemaps->tm[tmi_av] in rx_sta
==
mac_store_sta_get(rx_tei)->tx_tonemaps->tm[tmi_av] in tx_sta
Messages provided by the Standard allow to satisfy this need.
Moreover, Standard expects that the sets of tonemaps be removed if they have not been refreshed for more than 30 seconds. So, the RXCE will refresh its rx_tonemaps while TXCE will monitor the expiration date of its tx_tonemaps.
At last, a specific Sound MPDU can be sent to the rx_sta. For example, because no valid tonemaps are in the set of tx_tonemaps. A specific acknowledge is necessary to this type of MPDU, the Sound Complete Flag (SCF).

tx_sta
rx_sta

measure...

acquisition...
data
processing...

trames data

tx_tonemaps update

changed
rx_tonemaps

CEI

sound (reason)

sound acknowledge
measure...
measure...
et SCF
computation

acquisition...

acquisition...

Note : It exists any specific tonemaps with predefined index. So, even if no tonemap are valid, the tx_sta can use one of these tonemaps to transmit data. (MINI-ROBO, STD_ROBO, HS-ROBO).

Finally, the Channel Estimation is divided in two parts. The RXCE that accumulates measures, analyse it in order to generate any tonemaps and create CEI to send the sets of tonemaps to transmitters. RXCE is described in the second part. (RXCE process.) The goal of TXCE is to receive CEI, decode it, and update its tx_tonemaps. More, it will expire the sets when necessary.
Note : This document does not describe the 'bit loading', that is the way to compute the tonemaps from all the measures. (cf 'bit loading' documentation)

## TXCE
ce/inc/tx.h
TXCE is a state of the Control Plane. When CP receives an MME that is a CEI, it calls the main txce function with the TEI of the source station, the type of the CEI and the address of the MM_ENTRY.
void txce (txce_t *ctx, uint stei, u32 mmtype, u8 *mmentry)
This function is decoding CEI and update the set of tonemaps concerned by the source station of CEI. Its expiration date is postponed at 30 seconds more. Then, it looks through all its sets of tonemaps to expire it if necessary and to detect the next expiration date. At last, it reinitialises an alarm for this date. If alarm is triggered, an event is added in CP that will recall this main txce function as soon as possible.

Note : Interface with CP is not really defined. Following but temporary choices have been done :
- CP knows TEI of source station. (concerned question about table access of tei2mac_address.)
- CP knows to the type of the CEI.
- CP provides address of the MM_ENTRY (et not start of MME).
- Possibility of adding an event in CP.

CESAR run under ECOS. Date functions expressed in ECOS ticks (RTC), et alarm functions are available.
### Context.
ce/inc/tx.h
TXCE context (txce_t) consists of :
- A pointer to mac_store (to access to set of tonemaps).
- A pointer to CP_EVENT interface allowing to add a TXCE event.
- Handles to manage an ECOS alarm.
- The tonemask for CEI decoding. The tonemask describes all the used carriers among the usable carriers. CEI are relative to the used carriers , called too non-masked carriers. tonemaps are relative to the usable carriers.

#### Initialisation
txce_t *
txce_init (mac_store_t *mac_store_ctx, mac_config_t *mac_config_ctx, interf_t *interf)
Context is initialised by CP that provides 'mac_store', CP_event interface, and 'mac_config' where is stored the tonemask. This initialisation of the alarm is done in linking an rtc_clock of ECOS and in providing the callback when alarm is triggered. This callback, 'alarm_cb' is called in TXCE context in order to get reference of the CP_EVENT interface.

### Sequence.
ce/inc/tx.h
The txce function, called by CP, is mainly called when a MME has been received and detected as a CEI. Eventually, it can be called when a TXCE event is processed. (A TXCE event has been posted by the expiration alarm.)
txce (txce_t *ctx, uint stei, uint mm_type, u8 *mm_entry)
If a MM_ENTRY exists , then
Get tx_tonemaps of station defined by the STEI.
Call decoding function 'cei_decode' described in CEI chapter, with the set of tonemaps, the mm_type, the mm_entry and the tonemask as parameters. 'cei_decode' function update the expiration date of the set tx_tonemaps.
Call the expiration function, described in the 'Sets of tonemaps expiration' chapter that returns the nearest expiration date.
Restart alarm to trig for this new date.

get next event

MME
TXCE event
MME header
 decoding

CEI
stei, mm_entry, mm_type
entry?
get tx_tonemaps
 from stei and mac_store
CEI
 decoding
and
tx_tonemaps update
tx_tonemaps of stei
mm_entry, mm_type
stei
get tx_tonemaps of tei i
 expiration
current_date >
expiration_date?
get tx_tonemaps
 expiration
keep the nearest
expiration date
i Є all possilbles tei
TXCE
null mm_entry
mac_store_ctx
CP
event
list
reinit alarm

ECOS
alarm
Add TXCE
 event

triggered

### Sets of tonemaps expiration
cyg_tick_count_t txce_expiration_tonemaps_management (txce_t *ctx)
This function is called each time a CEI is received. It can be called when the alarm has triggered and CP has processed a TXCE event.
Not optimised at all:
It look through all the possible TEI, if the station exists and, if it is, check the expiration date (expire if necessary). Then, it returns the neartest expiration date it has found.
It is not optimised because it would be necessary to manage a list keeping references on set of tonemaps. And a difficulty appears when a station is deleted from the mac_store. The simple solution has been chosen, but a best solution could be study.

### CEI Reception.

cf. CEI Decoding
Notes :
- CEI can ask a tonemap became invalidate. then, memory must be freed. But PBPROC can receive a invalidation from a Sound acknowledge. Can PBPROC free it? If not, how to do?
- A tonemap can not be changed. It can only be deleted. The PBPROC has priority over the CP, so TXCE must atomically prevent tonemap access before free it.
- The interval of a set tx_tonemaps can be changed. The PBPROC can being in access on it. An atomic swap system between current interval and next intervals avoid the trouble of shared data.

## The RXCE process
The RXCE is a process that runs under ECOS, like the SAR or the CP. Its priority is the lowest. A priori, 'bit loading' computation duration seems to be variable. We can imagine that RXCE be integrated in CP, but it could give the behaviour of the CP unstable (in time point of view).
Goals of RXCE are :
- To store measures done by DSP on each received MPDU.
- To use measures to create tonemaps and to define intervals for each known station of the AVLN. (set of tonemaps rx_tonemaps). This part is not described in this document. (cf 'bit loading' documentation).
- To create CEI when rx_tonemaps is changed or to refresh it before the remote station expires it.
- To give information to PBPROC to acknowledge a sound MPDU.
- To give information to PBPROC about its need of measures. (TBD, no interface). For instance, NOISE_NRJ and NOISE_NRJ_SYMBOL are get up from all ROBO mode modulated frames, and from 'with enough symbol' frames.

### Environment.

mac_store

stations sta_t
rx_tonemaps
rxce_status
(not used)
pbproc_

rxce_
sar_

sound reason
 code

sound complete
flag

measurement

allocated
blocks
pb_pool

DSP

Data
Memory

(mpdu,
measurement)
PB_DMA

A
F
E

interrupts

PLC
cp_
cei
mme

TX...

### Process description.

t
MPDU
cyg_semaphore_wait 'job'
pbproc_
pbproc_
sar_
pbproc_need_scf?

y
a cei_param?
sound_param
mpdu_measure_store

cei_param_fifo

pbproc_need_scf_cb
(if sound mpdu)
sar_noise_add_cb
post (measurement)

y

'job' semaphore

eventually
n
n
compute_scf
pbproc_scf
rxce_cei_generate
rxce_
next_measure_compute

rxce_tonemaps_
refresh_management

timeout
an mpdu
measure?

y
post (SRC)
post (CEI)
post (CEI)
post (CEI)

ce/inc/rx.h
RXCE process is waiting on a counting semaphore ECOS and following events can increment the counter. (called 'job') :
- When a sound MPDU is received, PBPROC must acknowledge. So that a SCF is required to indicate if RXCE wants more sound MPDU or not.(cf Sound Complete Flag estimation). For this purpose, PBPROC callback an RXCE function that saves reception conditions in its context : The Sound Reason Code, the source TEI of MPDU. More the callback saves the fact that PBPROC is waiting for a SCF value and, add finally a new job. When RXCE thread can run, it checks at first if PBPROC is waiting for a SCF, and if it is, analyse reception conditions then informs PBPROC about its value to return.
  Note 1 : PBPROC will return 'SCF = false' if it didn't have any information from RXCE.
  Note 2 : It may be necessary to create a CEI.
- At the end of MPDU, any measures has been done by DSP and written in several on-chip memories and in each descriptor of data Pbs.(cf. Measures storage) The SAR is responsible of providing these measures to the RXCE by callback. Measures will be stored in the 'mpdu_measure_store'. Once stored, a job is added in the semaphore. When RXCE thread can run, if it is not necessary to compute a SCF, neither to create a CEI, it computes the oldest measures present in the mpdu_measure_store.
  Note : It may be necessary to create a CEI.
- The last reason to add a job is the need of creating a CEI and to send it thanks to CP. Three situations can cause the creation of a CEI.
  1. When RXCE analyse the reception condition of a sound MPDU. (cf Sound Complete Flag estimation.)
  2. A set of tonemap have been changed after measures computation (cf 'bit loading' documentation).
  3. To refresh a set of tonemaps. The refreshing works by adapting the waiting duration on the semaphore according to the next refresh date.
In each case, to cause the creation of a CEI, any parameters must be added in the 'cei_param_fifo'. (cf. Storage of a CEI param)
When RXCE can run, if it is not necessary to compute a SCF and if the 'cei_param_fifo' is not empty, it creates the CEI thanks to stored parameters and informs CP it can be sent.(cf. CEI generation )

### Context.
The context of RXCE (rxce_t) consists of :
- A pointer to mac_store. (to access to the sets of tonemaps)
- A pointer to the tonemask. (to create CEI from non-masked carriers and to analyse measures)
- An ECOS semaphore.
- A 'sound_param' consists of the Sound Reason Code and the STEI of the last received sound MPDU.
- A boolean indicating if PBPROC need a SCF : pbproc_need_scf. It is reset to 'false' once the SCF is computed.

### Sound Complete Flag estimation.
For various reasons, a station may decide to forward a sound MPDU rather than data. This reason is informed in the FC. Thus, RXCE thread can analyse this reason, and ask the transmitter to continue or stop sending sound MPDU. The receiver may decide to generate a CEI so that transmitter update its set of tonemaps.
For example :
A station tx_sta sends a sound MPDU because it has not a valid default tonemap. The destination station (rx_sta) recognize that no tonemap default has been computed. As long as it need additional measures, PBPROC will acknowledge with a 'false' as SCF. Then, once the default tonemap is computed, it will return 'true'.

.Extract from the norm HP_AV 1.1 on the transmission of a Sound MPDU :
Sound Reason Code is an 8-bit field that indicates the reason for transmitting the Sound MPDU. The interpretation of this field is shown in Table 4-42. This field is valid only in Long Sound MPDUs and shall be set to 0x00 in all Sound ACKs.

SRC num	SRC Value	Interpretation
SRC0	0x00 ­ 0x03	Reserved
SRC1	0x04 ­ 0x1F	Sound MPDU transmitted to obtain the Tone Map corresponding to a TMI_AV, which has been specified by the receiver in the intervals information but is not recognized by the transmitter.The five LSBs of this field contain the TMI_AV (refer to Section 4.4.1.5.2.13).The receiver may resend the Tone Map Data (TMD) corresponding to TMI_AV or it may resend all valid Tone Maps upon the reception of this Sound Reason Code.
SRC0	0x20 ­ 0xFB	Reserved
SRC2	0xFC	Sound MPDU transmitted to indicate a Tone Map error condition detected at the transmitter. Receiver shall resend all valid Tone Maps.
SRC3	0xFD	Sound MPDU transmitted as part of Initial Channel Estimation.
SRC4	0xFE	Sound MPDU transmitted in an interval where receiver has indicated that no AC Line Cycle adapted Tone Maps are available.
SRC5	0xFF	Sound MPDU transmitted in an interval specified as Unusable by the receiver.

#### Sequence.
When a sound MPDU is received by a station, its PBPROC get up measures of SRC et STEI from the FC thanks to an RXCE callback.
pbproc_need_scf_cb (void *user, uint stei, uint src)
This callback update information in RXCE context, and set the pbproc_need_scf boolean.It is done at the end of the FC decoding. So there is still a sound frame duration to evaluate the SCF. More SAR has no reassembly to do. The RXCE thread compiles data of 'sound_param' and informs its decision thanks to the PBPROC function :
pbproc_send_scf(bool).
Note : If PBPROC doesn't receive SCF from RXCE process, it will acknowledge with a 'false' SCF.
Interface with PBPROC is not defined. Fonctions pbproc_need_scf_cb (void *user, uint stei, uint src) , pbproc_send_scf(bool) and callback recording are not fixed.
#### Sound Reason Code compilation.
void rxce_scf_compute (rxce_t *ctx)

Choices to compute the SCF according to the SRC are not forced by the Standard. Except for the SRC2, and an option for the SRC1. The following describes strategy that could be changed :

SCF 1

interval
 with
a valid
 tonemap?
post (CEI) with
cei_param.tmi = src
post (CEI) with
cei_param.tmi = NULL
(all valid TM)
       yes

SRC1

SRC2

SRC3

SRC4
SRC5
SCF 1

tonemap
default
valid?
ce in
initial
 step?
       yes
SCF 1
       yes
post (CEI) with
cei_param.tmi = NULL
(all valid TM)
SCF 0

invalid
rx_ tonemaps
SCF 0

SCF 1
SCF 0
interval
 with
a valid
 tm?

       yes

For more details about the 'cei_param', cf. The 'cei_param' module.

### Measures storage.
ce/inc/mpdu_measure_store.h
During the reception and the demodulation of an MPDU, any measures are done by the DSP and written in the on-chip memory. One of the goals of PBPROC is to get up these measures. To inform the PBPROC about the need of RXCE, no interface has been defined and it is considered that conditions are fixed : “NOISE_NRJ and NOISE_NRJ_SYMBOL are get up from all ROBO-mode modulated frames, and from 'with enough symbol' frames”. These measures are given to the SAR in any 512-bytes linked blocks called phy_chandata. It exists several type of phy_chandata according to the memory they come from.
The type of phy_chandata are defined in hal/phy/pbdma.h. (cf. 'Phy_chandata')

In addition, during the transfer of data, PBDMA fill in the descriptors with measurements taken individually on each PBs. The pb_measurement structure also appears in hal/phy/pbdma.h.
For more details about the measures, cf 'bit loading' documentation.
RXCE need to get these measures and to know the reception conditions : (arrival date, source station, tonemap used.) This data are present in the structure pbproc_rx_params, defined in /mac/pbproc/pbproc.h. During the reassembly (SAR), an RXCE callback stores all the pb_measurement, all the phy_chandata, and the pbproc_rx_params of the MPDU.

mac/sar/sar.h
typedef bool
(*sar_measurement_cb_t)
(void *user, pbproc_rx_params_t *rx_params,
uint pb_nb, blk_t **first, blk_t **last,
pb_t *chandata_first, uint nb_chandata);
et the corresponding callback recording :
sar_init_measurement_cb (sar_t *ctx, sar_measurement_cb_t sar_measurement);

The 'user' variable is used to get babk the RXCE context, initialised by SAR with the following function :
sar_init_measure_context (sar_t *sar, void *user);

In the callback, SAR get the memory provided by RXCE to store the pb_measurement, give pbproc_rx_params and give the first phy_chandata of the list. To provide the memory, we use the fact that the RXCE can not be interrupted during the reassembly. So, it will not be able to access to the pb_measurement before SAR has end to fill in the memory.

SAR not interruptible by RXCE

sar_measurement_cb

 - pb_measurement blocks allocation.
 - first chandata recovery.
 - pbproc_rx_params recovery.

X
 - Fill in of provided blocks with pb_measurement extract from data PB of the MPDU, and written by the PBDMA .

#### 'Pb_measurement'.
ce/inc/mpdu_measure_store.h
For each reassembly PB, a pb_measurement must be copy by the SAR in the by-RXCE allocated blocks. The RXCE allocates a number of block depending on the size of a pb_measurement and the number of PB to reassembly. These blocks are chained and are considered as blk_t for the SAR but becomes a pb_measurement_list_t for the RXCE. This structure has a pointer to the pb_measurement data, a pointer to the next pb_measurement_list and an integer that informs about the number of valid pb_measurement in the data block. The value of the last field is written by RXCE during allocation.
struct pb_measurement_list_t
{
struct pb_measurement_list_t *next;
pb_measurement_t *data;
uint pb_nb;
}

next
data
pb_nb
...
pb_measurement
...
...

next
data
pb_nb
...
pb_measurement

X

Values of pb_nb are at the maximum value, except for (eventually) the last one. For example, if the MPDU consists of 158 PBs, there is 158 pb_measurements to store. But only 128 pb_measurement can be store in a block. (sizeof(pb_measurement) = 4 and sizeof(blk_data) = 512.) The callback will allocate two blocks, and initialize the first pb_nb with 128 and the last one with 158-128 = 30.

Note :
It is planned for a future version, that the SAR reassembly an MPDU in many times. In this case, the callback shall give back the last block in pb_measurement already allocated but not completely filled in. More callback must indicate where to start to write. Today, it is anticipated for the allocation of pb_measurement_list but not for the rest of code. So, the code in question may seem inconsistent with the rest.

#### 'Phy_chandata'.
hal/phy/pbdma.h
RXCE get the first phy_chandata and size list from the SAR. But the list may consist of a set of sub-list with different type. The callback separates these sub-chain thanks to 'type' information provided in the phy_chandata descriptors. For the SAR, blocks are pb_t but RXCE can considere it as phy_chandata :
enum phy_chandata_type_t / { / PHY_CHANDATA_TYPE_NO_MEMORY_READ, / PHY_CHANDATA_TYPE_NRJ, / PHY_CHANDATA_TYPE_NRJ_SYMBOL, / PHY_CHANDATA_TYPE_SPECTRUM_TRUNC, / PHY_CHANDATA_TYPE_SPECTRUM_RE, / PHY_CHANDATA_TYPE_SPECTRUM_IM, / PHY_CHANDATA_TYPE_DATA_LLR, / PHY_CHANDATA_TYPE_COPY_I_LLR, / PHY_CHANDATA_TYPE_COPY_Q_LLR, / PHY_CHANDATA_TYPE_COPY_VOTE_COEF, / PHY_CHANDATA_TYPE_NB / }	struct phy_chandata_t / { / blk_t blk; / BITFIELDS_WORD / ( / u32 size:8;, / u32 last:1;, / u32 type:4;, / u32 :7;, / u32 address:12; / ) / };

The 'type' field allows to distinguish the sub-chain. The callback build a set of pointers to the start of each sub-chain :
phy_chandata_t *head[PHY_CHANDATA_TYPE_NB]
The number of phy_chandata provided by the callback parameters allows to know the end of the list : Indeed, the last block does not necessarily points to a null pointer.

Example :
This following list is provided thanks to a pointer 'first' that points to the start of the list.

next
data
...
type = T1
...
...
noise_type_1
...
...

next
data
...
type = T1
...
...
noise_type_1
...
...

next
data
...
type = T2
...
...
noise_type_2
...
...

first

After callback, we get a set of sub-lists :

next
data
...
type = T1
...
...
noise_type_1
...
...

next
data
...
type = T1
...
...
noise_type_1
...
...

next
data
...
type = T2
...
...
noise_type_2
...
...

head[T1]
head[T2]
X

X

#### 'mpdu_measure'.
ce/inc/mpdu_measure_store.h
RXCE stores all the measures in a structure with pointers to each of them.

mpdu_measure_t
{
pbproc_rx_params_t *rx_params
pb_measurement_list_t *pb_head
phy_chandata_t *chandata_head[PHY_CHANDATA_TYPE_NB]
}

#### 'mpdu_measure_store'.
ce/inc/mpdu_measure_store.h
In order not to slow the SAR, RXCE accumulates measures that will be computed later in RXCE thread. For this, a static array of mpdu_measure maintained as a FIFO is implemented, the mpdu_measure_store :
struct mpdu_measure_store_t
{
       /** Reserved space to store mpdu measures.*/
       mpdu_measure_t store[MPDU_MEASURE_STORE_SIZE];
       /** head of store. To get the oldest mpdu measure.*/
       uint head;
       /** tail of store. To put a new mpdu measure inside.*/
       uint tail;
       /** Number of mpdu measures in store.*/
       uint measure_nb;
}

A function allows to read the oldest mpdu_measure stores in the mpdu_measure_store:
mpdu_measure_t * mpdu_measure_store_get(mpdu_measurement_store_t *ctx)
It is called when measure computation can be run with the rxce_measurement_compute function. (cf bit loading documentation)

A function allows to write a new mpdu_measure and add it in the mpdu_measure_store if it is not full. This function is called back bu the SAR. Any blocks are allocated for pb_measurement and the list of phy_chandata is broken. If the mpdu_measure_store is full, it frees the pointed phy_chandatas and pbproc_rx_params and returns 'false'.

bool
mpdu_measure_store_append (mpdu_measure_store_t *ctx,
pbproc_rx_params_t *rx_params, uint pb_nb,
        pb_measurement_list_t ** first, pb_measurement_list_t **last,
phy_chandata_t *noise, uint chandata_nb)
More, a function is enable to free all memory pointed by an mpdu_measure :
bool
mpdu_measure_store_release (mpdu_measure_store_t *ctx,
mpdu_measure_t *measure)

#### Acquisition sequence.
Call the mpdu_measure_store_append that :
if store is full :
free phy_chandata and pbproc_rx_params and returns 'false'
else :
Recovery the next mpdu_measure available of the store.
Allocate the necessaries blocks and fill the pb_head with the first allocated block.

void
    mpdu_measure_pb_add (mpdu_measure_t *measure, uint pb_nb, pb_measurement_list_t **first, pb_measurement_list_t **last)

Recovery address of the first phy_chandata, make the set of sub-list and fill the chandata_head[]

void
    mpdu_measure_chandata_add (mpdu_measure_t *measure, phy_chandata_t *chandata_head, uint phy_chandata_nb)

Returns 'true'.

At last, if frame_measurement_append has returned 'true', a new job is added in the semaphore of the RXCE thread.

### CEI generation.
The CEI generation is done in two steps. First, parameters needed for the creation of the message are recorded. Then, when RXCE thread decide to create a message, it recovery the stored parameters, create CEI, and sent it via the CP.
ce/inc/cei.h
To create a CEI :
1. Get a buffer from the CP.
2. Know the set of tonemaps concerned, the tonemap to encode if necessary, and the tonemap to replace if exists. This information is stored in a structure called 'cei_param'. (cf. The 'cei_param' module)
3. Choose the type of CEI to create.

To send a CEI via the CP :
The destination TEI, the length of the message and the type of the CEI must be known by CP.
#### The 'cei_param' module.
ce/inc/cei_param.h
A structure cei_param is used to store parameters of a new CEI to generate :
 struct cei_param_t
{
       /** Set of tonemaps concerned */
       tonemaps_t *tms;
       /** tonemap index to encode */
       uint new_tmi;
       /** tonemap index to inactive */
       uint old_tmi;
       /** Destination tei use by CP to get the MAC ADDRESS */
       uint dtei;
}

As described in the RXCE process, it is necessary to accumulate a set of cei_param in a list to report the CEI generation : the cei_param_fifo. The module provides function that allow to initialize the fifo, add a cei_param and get the oldest.
 struct cei_param_fifo_t
{
       /** Space reserved to store the cei_param_t */
       cei_param_t list[CEI_PARAM_FIFO_SIZE];
       /** Index of the next cei_param_t to read */
       uint reader_index;
       /** Index of the next cei_param_t to write */
       uint writer_index;
       /** Number of valid cei_param_t stored in the list. */
       uint number;
};

cei_param_fifo_init (void)
bool cei_param_add (cei_param_t *) add the pointed content in the fifo.
cei_param_t *cei_param_get( void) returns a pointer to the oldest cei_param stored in the fifo.

ce/inc/rx.h

void
rxce_add_cei_job (rxce_t *ctx, tonemaps_t *tms,
uint new_tmi, uint old_tmi, uint dtei)

This function used in the RXCE process, allows to add a job once cei_param are stored. More, it updates the refresh date of the set of tonemaps, considering that the CEI has created now. The new refresh date = current_date + RXCE_TONEMAPS_REFRESH_PERIOD.
The RXCE_TONEMAPS_REFRESH_PERIOD is defined by :
RXCE_TONEMAPS_EXPIRATION - RXCE_TONEMAPS_REFRESH_MARGIN.
RXCE_TONEMAPS_EXPIRATION is 30 second, (Standard)
RXCE_TONEMAPS_REFRESH_MARGIN is the worst estimation between the date when cei_param has been stored, and the date when the set of tonemaps has really been updated.

#### Interface CEI with the CP.
Interface with the CP is not defined. The following description is tentative.
cp/interf/interf.h :
To create the MME header, the CP must find the mac_address. For this, RXCE provides the DTEI. Then, CP must write the type of the MME and informs its length to the other layer.
mme_t { uint dtei, uint length; uint mm_type, u8 *mm_entry; }

to get a buffer :
mme_t *interf_mme_get (void);

Once mm_entry is written, RXCE gives back it with the MME information filled in.
void interf_mme_send (mme_t *mme);
DTEI is stored in the 'cei_param', and length and mm_type are known after creation (cei_decode) that returns the cei_created_status structure.
#### Sequence.
rxce_cei_generate ()
{
  cei_param_t *param = cei_param_get();
  mme_t *mme = interf_mme_struct_get();
  cei_created_status_t cei_created =
cei_create (mme->buf, tonemask, param->source_tms,
param->new_tmi,param-> old_tmi);
  mme->dtei = param->dtei;
  mme->length = cei_created.length;
  mme->mm_type=cei_created.mm_type;
  interf_send (mme);
}
### Set of tonemaps refresh.
cyg_tick_count_t rxce_tonemaps_refresh_management (rxce_t *ctx)
This function is called each time the RXCE thread has run.
Not really optimised :
It looks through all the possible TEI. if the station exists , it checks the refresh date of the set rx_tonemaps. If the current_date is greater than the refresh date, it prepares a new CEI to generate. Finally, it returns the nearest refresh date it has found. The time-out of the semaphore is then reinitialised with this nearest refresh date.
It is not optimised because it is necessary to manage a list keeping references on set of tonemaps. And a difficulty appears when a station is deleted from the mac_store. The simple solution has been chosen, but a best solution could be study.

© 2006 SPiDCOM Technologies, ALL RIGHTS RESERVED

SPC, SPR, SCR, SVR are trademarks of SPiDCOM Technologies.
All other products or services mentioned herein may be trademarks of their respective owners.

Notice: No part of this publication may be reproduced or transmitted in any form or by any means, electronic or mechanical, including photocopying and recording, or stored in a database or retrieval system for any purpose without the express written permission of SPiDCOM Technologies.

SPiDCOM Technologies reserves the right to make changes to this specification at any time without notice and assumes no responsibility for its use. This specification contains the most current information available at the time of publication.