Ecos HAL specifications / CESAR - FULMINATA A1: 2007/05/30 / Jean-Philippe SAVE

References
[Ref1]	eCos Reference Manual :
//Gevrey/spidcom/tek/Projets/0702-01__CESAR/04__Documentation/02__Ecos/01__Documentation/ecos-2.0-ref.pdf

[Ref2] Embedded Software Development with eCos :
//Gevrey/spidcom/tek/Projets/0702-01__CESAR/04__Documentation/02__Ecos/01__Documentation/dvlpmt-with-eCos.pdf

[Ref3] Maximus Generals Specifications :
//Gevrey/spidcom/tek/Projets/0702-01__CESAR/04__Documentation/01__Specs/12__Fulminata_Maximus/fulminata_general_specs_v0.odt

[Ref4] Maximus Station Specifications :
//Gevrey/spidcom/tek/Projets/0702-01__CESAR/04__Documentation/01__Specs/12__Fulminata_Maximus/fulminata_station_specs_v0.odt

Acronyms
HAL : Hardware Abstraction Layer / VSR : Vector Service Routine	ISR : Interrupt Service Routine

# Introduction
The aim of this document is to provide specifications of eCos Hardware Abstraction Layer for our specific target : Maximus.
This new target is based on the eCos synthetic target, which can run an eCos instance on a PC with a Linux running. The difference between these two target (Maximus vs Synthetic) is that in Maximus we want to communicate this the maximus simulator and not directly with Linux.
This document is divided into four parts which detail each eCos HAL key-point :
1°/ the cache control,
2°/ the interruption management,
3°/ the input/output management,
3°/ the diagnostic communications,
4°/ the initialization procedure.

# Cache control
## Introduction
Presence of cache memories is, of course, hardware dependent, so the HAL have to manage it consequently.
At least, the HAL have to enable/disable cache used, start a synchronization...

## Processing
With our target Maximus, we use a Linux OS under a PC (i386-processor). So we use the RAM of the PC and consequently, the cache management is not used for this target whether instruction or data cache.

## Structures, Defines and APIs
Although we don't use cache control, certain macros have to be present for a communication with the rest of eCos :
HAL_ICACHE_ENABLE()
HAL_DCACHE_ENABLE()

HAL_ICACHE_DISABLE()
HAL_DCACHE_DISABLE()

HAL_ICACHE_SYNC()
HAL_DCACHE_SYNC()

HAL_ICACHE_INVALIDATE_ALL()
HAL_DCACHE_INVALIDATE_ALL()

HAL_ICACHE_IS_ENABLED(_state_)
HAL_DCACHE_IS_ENABLED(_state_)

# Interruption management
## Introduction
Although we use a target which not have a physically hardware, a management of interruptions must however be present. This management of interruptions gathers, for eCos, several parts :
1°/ exceptions,
2°/ reals interrupts,
3°/ clock and ticks management.

## Processing
As we see in the Ref 3 and Ref 4, each eCos Maximus target can communicate with two layers : SCI and PHY-Ctrl. So, for the eCos HAL these two layers “represent the hardware”.
First of all, let us remember the interruptions operation for a target which have a real hardware. Each interruption arrival, whether it is real interruptions or exceptions, starts a VSR. And this is the VSR which will call the good ISR recorded preliminary by an application.
The following figure represent a classical interrupt procedure :

Interrupt
VSR
ISR

HAL
Application

Recorded previously

But with our Maximus target, we adopt two differents methods depend on interruption type (exception and real interruption).

### Exception procedure
Exceptions occurred when an error is detected by the processor (the hardware). In our particular case the processor is ordered by Linux so exceptions will start a specific Linux Signals giving the procedure described in the following figure :

VSR
ISR

HAL
Application
Recorded previously

Signal

Linux
Signal
Handler

Recorded previously

Exception

According to this new procedure, two records are needed. But be careful, the recording mechanism is managed on one hand by the SCI layer for SIGNAL handler (sci_callback_register) and on the other hand by the eCos HAL layer for the correct ISR (cf. Chapter 3.3).

### Interrupt procedure
Interruptions can be divided into two different part : hardware interrupts and tick timer for clock. But for our Maximus target the procedure will be the same.
This time, we will not choose the Linux Signal method but the IDLE thread method. Maximus is a simulator so processor timing is unlimited and we will only use two threads : one for our code and the other for the IDLE mode.
With the hypotheses described above an interrupt can occurred only when we are in IDLE thread. In this thread we only are going to wait for interrupt which are given by the SCI Layer.
The following figure summary the Interrupt procedure :

VSR
ISR

HAL
Application
Recorded previously

Wait for
Interrupt

SCI
IDLE
Thread

Interruption

+

Let us see now the choices retained for the various signals, the VSR as well as the ISR.

### Signals
Signals are managed by the SCI layer so in this part we only detail the different signals handler waiting by our new eCos HAL.
We can split signals into different parts depending on the exception cause (SIGILL, SIGBUS, SIGFPE and SIGSEGV). But for us, the handler procedure will be the same.
### VSR
The figures below describe the complete interrupt treatment chain but, all signals and “idle”event haven't to start a specific VSR, for example when an exception arrive, in our Maximus target starting a VSR has no sense, you have to stop anything now whatever the exception, so the signal handler differentiation is enough.
We use the VSR to differentiate events coming from the same signal and “idle” and to manage interrupt level.... so for interruptions and tick signal. We assigned tick signal to the ISR 0 consequently, only one VSR will be used.
### ISR
Each ISR is attached and detached to an handler by an application. ISR 0 correspond to the tick so, the 31 others are free to use.
## Structures, Defines and APIs
Defines needed for interruption management :
CYGNUM_HAL_INTERRUPT_RTC
CYGNUM_HAL_ISR_MIN
CYGNUM_HAL_ISR_MAX
CYGNUM_HAL_ISR_COUNT
CYGNUM_HAL_EXCEPTION_ILLEGAL_INSTRUCTION
CYGNUM_HAL_EXCEPTION_DATA_ACCESS
CYGNUM_HAL_EXCEPTION_FPU
CYGNUM_HAL_EXCEPTION_MIN
CYGNUM_HAL_EXCEPTION_MAX
CYGNUM_HAL_EXCEPTION_COUNT
CYGNUM_HAL_VECTOR_SIGNAL
CYGNUM_HAL_VSR_MIN
CYGNUM_HAL_VSR_MAX
CYGNUM_HAL_VSR_COUNT

Interrupt State Control Macros :
HAL_ENABLE_INTERRUPTS()
HAL_DISABLE_INTERRUPTS(_old_)
HAL_RESTORE_INTERRUPTS(_old_)
HAL_QUERY_INTERRUPTS(_old_)

ISR and VSR Management Macros :
HAL_INTERRUPT_IN_USE(_vector_, _state_)
HAL_INTERRUPT_ATTACH(_vector_, _isr_, _data_, _object_ )
HAL_INTERRUPT_DETACH(_vector_, _isr_)
HAL_VSR_GET(_vector_, _vsr_)
HAL_VSR_SET(_vector_, _vsr_, _poldvsr_)

Interrupt Controller Management Macros :
HAL_INTERRUPT_MASK(_vector_)
HAL_INTERRUPT_UNMASK(_vector_)
HAL_INTERRUPT_ACKNOWLEDGE(_vector_)
HAL_INTERRUPT_CONFIGURE(_vector_, _level_, _up_)
HAL_INTERRUPT_SET_LEVEL(_vector_, _level_)

Specifics Clock Macros :
HAL_CLOCK_INITIALIZE( _period_ )
HAL_CLOCK_RESET( _vector_, _period_ )
HAL_CLOCK_READ( _pvalue_ )
HAL_DELAY_US(_us_)

# Input/Output management
## Introduction
Although we use a target which not have a physically hardware, a management of Input/Output can however be present. This management must allow access to device registers independent of the architecture.

## Processing
In our platform Maximus, IO access to devices does not really exist, there is no mapping between addresses, so access to a register is like access to an address.

## Structures, Defines and APIs
Typedef used to address registers :
HAL_IO_REGISTER

Macros need for devices registers access :
HAL_READ_UINT8( _register_, _value_ )
HAL_WRITE_UINT8( _register_, _value_ )
HAL_READ_UINT8_VECTOR( _register_, _buf_, _count_, _step_ )
HAL_WRITE_UINT8_VECTOR( _register_, _buf_, _count_, _step_ )
HAL_READ_UINT16( _register_, _value_ )
HAL_WRITE_UINT16( _register_, _value_ )
HAL_READ_UINT16_VECTOR( _register_, _buf_, _count_, _step_ )
HAL_WRITE_UINT16_VECTOR( _register_, _buf_, _count_, _step_ )
HAL_READ_UINT32( _register_, _value_ )
HAL_WRITE_UINT32( _register_, _value_ )
HAL_READ_UINT32_VECTOR( _register_, _buf_, _count_, _step_ )
HAL_WRITE_UINT32_VECTOR( _register_, _buf_, _count_, _step_ )
# Diagnostic communications
## Introduction
This chapter gathers the diagnostic part it is a method which makes it possible to transmit diagnostic informations on the system state. Generally, this system configures a UART to transmit informations via a serial port (it is one of the first debug methods).
Note that, for eCos, this diagnostic part is used with the call of functions like printf…

## Processing
In our case, Maximus target doesn't have any serial link of course, thus the diagnostic part will only make transfer to the lower layer : the SCI layer. We choose a Linux pipe communication system to do that.

## Structures, Defines and APIs
HAL_DIAG_INIT()
HAL_DIAG_READ_CHAR(_c_)
HAL_DIAG_WRITE_CHAR(_c_)

# Context switching procedure
## Introduction
Once again this procedure of context switching is hardware dependent and thus platform dependent.
The platform dependent part is not on the other hand majority since it step in only on the level of the recording processor registers.

## Processing
For our Maximus target, we are based on a i386 linux target thus, the processor registers to save are the i386 registers.
In our particular case, the context saving when interrupts occur is not obligatory. Indeed, any interruption comes from a Linux signal handler, it is thus the Linux system which save the processor registers before switching in interruption mode.
In conclusion only thread switching context is needed.
## Structures, Defines and APIs
Typedef for registers saving :
HAL_SavedRegisters

Macros for thread switching context :
HAL_THREAD_INIT_CONTEXT( _sparg_, _thread_, _entry_, _id_ )
HAL_THREAD_SWITCH_CONTEXT( _fspptr_,_tspptr_ )
HAL_THREAD_LOAD_CONTEXT( _tspptr_ )

# Initialization procedure
## Introduction
The system initialization implies several stages and particularly stages in connection with the hardware. Let us point out the traditional procedure awaited by the system eCos :
- start a soft reset,
- put the processor in a simple and known state (disable cache interrupt...)
- start the hardware initialization (enable cache, MMU, memory controller, Interrupts, clock....)
- prepare stack area,
- clear .bss part,
- invoke constructors,
- start eCos.

## Processing
In Maximus target, most of these previous stages are not needed because it's Linux which started our maximus eCos.
We only have to initialize our “hardware”, invoke constructors and start eCos. Indeed we don't have cache MMU...
For our pseudo-hardware initialization we just give our Linux signal handlers to the SCI layer and prepare VSR and ISR connection structures.

## Structures, Defines and APIs
Start function gives by the linker script : _start
Functions wishes for our specific platform :
_linux_entry()
maximus_hardware_init()

# Other key-points
Some defines and macros are needed by eCos and are hardware dependent so present in the HAL. It not possible to classify it so here it is.

## Thread IDLE mode
When you can do when a thread is in IDLE mode is precise in this Macro :
HAL_IDLE_THREAD_ACTION( _count_ )

## Stack size
Some macros which define each stack size :
CYGNUM_HAL_STACK_FRAME_SIZE
CYGNUM_HAL_STACK_CONTEXT_SIZE
CYGNUM_HAL_STACK_INTERRUPT_SIZE
CYGNUM_HAL_STACK_SIZE_MINIMUM
CYGNUM_HAL_STACK_SIZE_TYPICAL

## Endian-mode
Endian mode is processor dependent and for our Maximus target we apply the i386 endian mode. An eCos define is needed for this : CYG_BYTEORDER.

## Compilation optimization
There is only one mandatory macro for compilation optimization : HAL_REORDER_BARRIER()
but for our target we will not use it.

## Bit manipulations
Bit manipulations are mainly needed by eCos but we can find it even in the HAL.
So we will define these two macros :
HAL_LSBIT_INDEX(index, mask)
HAL_MSBIT_INDEX(index, mask)
## Platform RESET
The eCos system may need a reset action. To this way it use the following Macro :
HAL_PLATFORM_RESET()

## Global pointer
This pointer is only used for context switching but this time, it not for thread context but for eCos instances context (to switch between two eCos or between eCos and Redboot) :
CYGARC_HAL_SAVE_GP()
CYGARC_HAL_RESTORE_GP()

## Set/Long jump
Ecos provide a support for these two C functions :
CYGARC_JMP_BUF_SIZE
hal_jmp_buf[CYGARC_JMP_BUF_SIZE]
hal_setjmp(hal_jmp_buf env)
hal_longjmp(hal_jmp_buf env, int val)

# Files architecture
Let us see now how to organize in file the whole of the functionalities mentioned above.
We can based our architecture on the eCos synthetic HAL architecture with three directories :
- the first named common which is the higher layer of the HAL,
- the second named arch which depend on the architecture but not on the processor used,
- the third named i386 which only provided functions processor dependent.

History
A0	03/05/07	Jean-Philippe Save	Creation
A1	30/05/07	Jean-Philippe Save	Change Interruption procedure

Readers
Etienne Chevreau	SPIDCOM Technologies
Jérôme Lefranc	SPIDCOM Technologies
Celine Buret	SPIDCOM Technologies

Distribution
Etienne Chevreau	SPIDCOM Technologies

END