Fulminata general specifications / CESAR - FULMINATA 10/09/07 / Jérôme Lefranc

# Maximus presentation
## Introduction
Maximus is a Homeplug AV MAC simulator and validator. It aims to simulate real data communication through a complete AV MAC implementation embedded into an eCos real-time system.
Simulator uses several eCos system build in synthetic mode for x86 and which are able to really run into a linux PC. Each eCos running independently plays the role of an AV protocol stack into a virtual embedded processor and communicating outside through access points provided by the Maximus simulator.
The Maximus simulator provides a complete environment for these AV stacks to run and process data communication. This environment is composed of the following parts:
- Global clock simulator to give a common base time for process execution
- PHY interface to simulate the real Homeplug AV physical interface and data bus
- Function call interface to remotely act on running eCos systems
- System interface to launch and manage eCos systems
- Ethernet interface to simulate the real HLE interface
- Channel interface to manage the link quality between stations
- Scenario engine to create real data processing scenario by introducing at requested date data packet into the communication path
Each eCos systems running into PC host has several interfaces adapted to Maximus simulator:
- Dedicated Hardware Abstraction Layer (HAL) between eCos and simulator
- HAL for Homeplug AV PHY component
- HAL for Homeplug AV Higher Layer Entity
- HAL for Leon Timer 2
- Application stub dedicated to the wanted simulation / test
eCos systems and the simulator are communicating through a Simulator Communication Interface (SCI) provided by current OS of the PC host (here Linux). SCI uses a defined list of asynchronous messages to exchange data between eCos and the simulator.
## Architecture
See document “fulminata_maximus_architecture”.
# Maximus eCos
## Presentation
Each running eCos processes are intended to simulate a Homeplug AV station, with the AV embedded code inside. Homeplug AV software code is called Cesar code inside this document.
The AV station block is composed of several elements described into the following chapters.
The only unmodified parts are eCos OS and Cesar software code which are the same as into real hardware AV stations.
## SCI (Simulator Communication Interface)
This interface allows simulated AV station to communicate with the Maximus simulator.

Pipe
SCI
SCI
HAL
eCos
eCos
HAL
PHY
Cesar
Stub Common API
Application Stub
PHY
Function
Call
Network
Clock
Core Engine
Scenario Engine
GUI
eCos station
Maximus Simulator
System
HAL
HLE
Ethernet
Channel
HAL
Leon

All data transmitted through the SCI are asynchronous message based. Messages have variable length and have different types according to their content.
Types of message are described into the paragraph 3.2.
SCI uses pair of pipes to communicate with the simulator.
A specific API is used by simulated AV station to communicate through the SCI. This API is described into the paragraph 3.2.
## eCos HAL
eCos HAL is the adapted Hardware Abstraction Layer to run eCos with the simulator environment. Some parts are customized for SCI usage and other Maximus specific functionalities.
### RTC (Real Time Clock)
The RTC is not linked to a real counter, but uses the Maximus global Network Clock. When the eCos system needs a timer event, the request is transformed to a NetClock event request (see “fulminata_maximus_specs” for NetClock).
When the requested time occurs, the NetClock generates a timer interrupt request to the previously requesting simulated AV station through the SCI. This interrupt event is processed by the eCos HAL which relays the interrupt event to the eCos system.
RTC uses SCI “net_clock” message type to communicate with the NetClock.
### Serial interface
The simulated serial interface adds debug informations mainly coming from “printf” functions inside the AV station code. Serial interface uses “serial_data” message type to communicate with the simulator. Messages are only coming from the AV station to the simulator.
### Interrupts
Ecos HAL provides a way to generate simulated interrupt events. These interrupts are created by the HAL PHY to simulate the Homeplug AV physical interface (PHY Control). Interrupts are generated locally inside the AV station and no SCI message are used.
### Idle state
Idle state is a special AV station status occurring when the eCos system or the other code parts are not working. The whole system enter into idle state waiting for an event to happen. When entering into this state, a SCI “idle_state” message is generating from the AV station to the simulator.
## HAL PHY
The HAL PHY is the non-eCos part of HAL which simulates the Homeplug AV hardware interface, also called Maria.
### PHY Control
PHY Control is the control API of the Homeplug AV physical device. It is in charge of managing transmission and reception of AV packet from the physical medium.
All transmit request and receive events are simulated through an abstraction layer which generates some virtual physical setting or interrupts.
For transmission, API functions simulates registers setup and generate events for the Maximus simulator through the SCI. Messages type involved by the transmission are described into the “fulminata_station_specs” document.
For reception, HAL PHY Control receives messages generated by the Maximus PHY interface through the SCI. These messages are described into the “fulminata_station_specs” document. Some of these messages make the PHY Control generating an interrupt call simulation to the eCos HAL. This simulates interrupt requests from PHY device occurring while AV packets arrive.
### Bridge DMA
Bridge DMA is the API to manage the AV Mac Frame Streams (MFS). API is used to manage queued jobs processing, end of job interruption and delay due to job processing.
For processing delay, Bridge DMA requests a time event to the NetClock through the SCI. When the event occurs, an simulated interrupt is generated to the eCos HAL.
### Tone Map DMA
Tone Map DMA HAL layer simulates the tone maps and tone mask transfer needed by the PHY Control for packet rx/tx on the AV medium.
No timing nor interrupt event is needed for the simulation, so the API only provide the Cesar to Tone Map data transfer function.
### PB DMA
See document “fulminata_station_specs”.
## Application Stub
Application stub is the application layer above the Cesar code. It includes a common API and some dedicated code adapted to the test running inside the AV station.
Common API contains :
- Function call interface to remotely launch application stub functions with parameters from the Maximus simulator.
- Probe functions to register some variables and to remotely get access to them from the Maximus simulator. Probe functions are called through the classical function call described upside.
The dedicated code part is developed according to the wanted test we want to run inside the simulated AV station.
At final Cesar development step, the application stub will only contain the H1 access interfaces :
- CSAP (control plane SAP)
- ESAP (ethernet SAP)
- SSAP (streaming SAP)
### Function Call
Aim of function call API is to provide a way to remotely call functions inside the application stub from the Maximus simulator.
Software developer of application stub needs to register into his code the functions that are remotely accessible. Maximus simulator has access to these exported functions by sending a “function_call” message type through the SCI interface. Way to call a remote function with parameters is described into the paragraph 3.5.
When function returns inside the application stub, a “function_return” message type is sent to the Maximus simulator and directed to the function caller process. Function call and return messages are asynchronous.
TBD: Maximus simulator should obtain the list of available remote function by a “function_list” message type.
### Probe API
Probe API is a remote function available into all application stub. It allows the stub developer to register some code variables and make them available for a remote inspection.
Maximus simulator can ask for these variables through a “function_call” message type with “probe” function type. The “message_return” answer contains the value of the requested variable.
Details for how to probe a remote variable is contained into the “fulminata_station_specs” document.
## HAL HLE
The HAL HLE is the part that simulates the HomePlug AV Higher Layer Entity. See “fulminata_station_specs” for more details.
## HAL Leon Timer
The HAL Leon Timer is the part that simulates the Leon Timer 2. See “fulminata_station_specs” for more details.
# Maximus simulator
## Presentation
Maximus simulator is composed of a core engine, a scenario engine and an optional GUI.
The core engine is the minimal part to allow the simulator to work. It is composed by:
- Simulator Communication Interface (SCI) : to communicate with the simulated AV stations
- PHY Simulator : to simulate the Homeplug AV physical medium
- Function Call API : allow the simulator to remotely call functions inside simulated AV stations
- NetClock : global clock for scheduling all AV station events
- System API : provides all misc functions required by the simulator
- Ethernet : to simulate the sending and reception of Ethernet frames
- Channel : to simulate the link quality between AV stations
The core engine is the main simulator part which is managing the overall working of SCI, PHY interface, Function Call API, NetClock, System API, Ethernet and Channel.
## Simulator Communication Interface (SCI)
### Presentation
The Simulator Communication Interface (SCI) is the communication link between the Maximus simulator and the multiple simulated AV stations.
All communication is composed by messages inside data packets, sent through unidirectional pipes. For each simulator – AV station peer, 2 pipes are created with opposite directions.
### Message header
All message types have the same headers, describing the message content.

31 24	23 16	15 8	7 0
magic id
version	type	length
station id		msg id
NetClock High
NetClock Low
flags		reserved

Header size is 24 bytes long.
Description:
- magic id (32): always “MAXI”
- version (8): message protocol version; 0x01 for software version 1 or 0x02 for software version 2
- type (8): message type
- SCI_MSG_TYPE_NONE 0x00
- SCI_MSG_TYPE_NETWORK_CLOCK 0x01
- SCI_MSG_TYPE_FUNCTION_CALL 0x02
- SCI_MSG_TYPE_PHY 0x03
- SCI_MSG_TYPE_SYSTEM 0x04
- SCI_MSG_TYPE_ETHERNET 0x05
- length (16): message length without header
- station id (16): source or destination station id; in general, the process id of the simulated station
- msg id (16): unique message id for each station – simulator transaction
- 0x0001-0x7fff: request created by simulator
- 0x8000-0xfffe: request created by a station
- netclock high: high part of 64 bits NetClock value
- netclock low: low part of 64 bits NetClock value
- flags (16):
- SCI_MSG_FLAG_RESP 0x0001: if set, message is a response to a request; else, it is a request
- SCI_MSG_FLAG_ACK 0x0002: if set, message is an acknowledge to a request or a response
- SCI_MSG_FLAG_NEEDACK 0x0004: set an ack is requested from remote receiver
- SCI_MSG_FLAG_SYNC 0x0008: if set, a synchronous response is required
### Message protocol
Communication protocol is based on asynchronous message exchange.
Station id refers to the AV station inside the transaction. All transaction are done between an AV station and the simulator. If request is initiated by the simulator, destination is the AV station referenced by “station id”. If request is initiated by an AV station, destination is the simulator and “station id” refers to the requesting AV station.
Each message has a “message id” which is unique for the transaction. Id from 0x0001 to 0x7fff must be used when request is initiated by the simulator. Id from 0x8000 to 0xfffe must be used when request is initiated by an AV station.
During all the transaction, “station id”, “msg id” and type stay unchanged.
All transactions follow the current process between A & B:
1. A sends a request message to B. Flag SCI_MSG_FLAG_RESP is unset.
2. B receives the message and generates an acknowledge if flag SCI_MSG_FLAG_NEEDACK is set: SCI_MSG_FLAG_RESP is unset but SCI_MSG_FLAG_ACK is set, no payload is added and length = 0.
3. if asked, A receives the ACK message and returns to its current jobs.
4. When B is ready, it generates a response message with flag SCI_MSG_FLAG_RESP set and SCI_MSG_FLAG_ACK unset.
5. A receives the response and generates an acknowledge message if SCI_MSG_FLAG_NEEDACK is set: SCI_MSG_FLAG_RESP set, SCI_MSG_FLAG_ACK set and no payload (length = 0).
The “acknowledge” capacity is optional and will not be implemented in first version.
### Communication pipes
As each AV station is a process running a “maximus eCos” without TCP/IP stack, the only way to communicate with the simulator is to use pipes. Named pipe are preferred here with a name depending on the process number of the AV station.
Example:
- simulator launches AV station process #3165
- it creates 2 named pipes:
- maximus_sci_in_3165 as an input pipe for AV station
- maximus_sci_out_3165 as an output pipe for AV station
- AV station connects to these 2 pipe according to its known process number
When AV station process finishes, it cleans the 2 unused named pipes.
A AV station may crash, simulator must be insensible (or must process) to SIGPIPE and SIGIO signals.
AV station are implemented through the Station object class, and this class contains the pipe descriptors.
### Communication FSM
Pipes must be open with O_NDELAY option to never block the simulator in case of missing data. So, read or write process must be pending while the waited payload quantity is not reached.
As a read or write process may fail, a timeout must be managed for each transaction.
For message transmission, message descriptor is inserted into the “transmission queue”, the simulator waits until all data has been written, unless timeout has been reached. Then, if requested, simulator waits for the complete acknowledge message (unless timeout occurs). After optional ack, simulator puts the receiving pipe into its list of pending waited messages. Message descriptor is updated with result status.
For message reception, simulator is woken up by arriving messages from pipes. It reads all incoming messages and retrieve the pending message descriptor into the pending queue according to the “msg id” and the “station id”. Then the callback function referenced by the descriptor is called.
### missing FSM figures ###
### SCI Message
SCI messages are implemented under the virtual SciMsg class. This class defines and manages all SCI messages for SCI server and other API parts. Minimal members and functions common to all SCI messages are implemented into the virtual interface.
virtual class: SciMsg
see document “fulminata_maximus_architecture”
All extended SCI messages (PHY, NetClock, System, Ethernet and RemoteFunctionCall) are derived from this virtual class.
### SCI server
SCI server is a class instantiated once. It implements a receive server to process all incoming SCI messages from pipes. It also provides all functions to send a SciMsg object.
class: SciServer
see document “fulminata_maximus_architecture”
## NetClock
NetClock is the global time/event scheduler of the simulation system.
Each time an AV station is requesting a planned event, a “net_clock” request is addressed to the NetClock API. The request is enqueued into the NetClock event list, with an ordering according to the wanted time to start the event.
The NetClock register all “idle_status” messages coming from AV stations. When all AV stations are idle, the NetClock goes to the next coming event and send the new global time to all AV stations.
NetClock needs a time resolution compatible with the minimal clock tick of AV stations. This tick can be set to 1/25000000, equals to 40 ns. The real value must not be used, only the “tick unit”.
NetClock API must allows simulator to :
- add/insert an event
- remove an event
- list queued events
- send event message to target AV station
- send the new value of global clock to all stations
## PHY interface
PHY interface is the part which simulates the action of a real Homeplug AV physical medium.
In normal way of working, PHY interface receives Homeplug AV packet/data from AV station through the SCI layer with “av_data” message type. According to different AV data received, the PHY interface can:
- relay AV data to all or some AV station
- add a new event to the NetClock
- check AV data characteristics to determine if they can be received
## Function call
Function call API allows the simulator to remotely call functions inside the application stub of an AV station.
### Presentation
Aim of function call API is to provide a way to remotely call functions inside the application stub from the Maximus simulator.
Remote callable functions are identified through a unique string ID which allows the remote part inside stations to know which function to call.
When function returns inside the application stub, a “function_return” message type is sent to the Maximus simulator and directed to the function caller process. Function call and return messages are asynchronous.
### Function Call
Function call API is implemented through the FunctionCallManager.
class: FunctionCallManager
see document “fulminata_maximus_architecture”
### Function Call Message header

31 24		23 16	15 8	7 0
version		type	msg id
param nb	flags		reserved

Description:
- version (8): message protocol version; 0x01 or 0x02
- type (8): message type
- FUNCTION_CALL_TYPE_NONE 0x00
- FUNCTION_CALL_TYPE_REQ 0x01
- FUNCTION_CALL_TYPE_RSP 0x02
- msg id (16): unique message id for each function call and return
- param nb (8): number of parameters in the message data
- flags (8): -
- reserved (16): -
- data:
- function call id: null terminated string; id of the called function
- parameter list: for each parameter inside the function call message
- parameter id: null terminated string; id of the parameter
- parameter length (2): unsigned short; length of parameter data
- parameter data: binary content of parameter data
### Function Call message API
Function call message class FunctionSciMsg inherits from SciMsg. It implements all data process to create a function call raw message ready to be sent to the communication pipes.
## System API
System API contains all functions in relation with the PC host where simulator is running. API provides functions to :
- create/remove AV station
- dump debug from selected AV stations serial ports
- register/unregister an AV station
- receive idle message and process the event queue
## Ethernet
Ethernet package allows the simulator to send and receive Ethernet frames.
## Channel
Channel package allows to introduce channel perturbation on the system. Channel package provides functions to manage the link quality between AV station.
## Scenario management
See document “fulminata_maximus_scenario_engine”.

History
A0	03/20/07	Jérôme Lefranc	Creation
A1	10/09/07	Céline Buret	Update document according to the Maximus scenario engine specifications (version A1) and the Maximus architecture (version A2). / Add the Ethernet and Channel simulator parts, and the CL HAL station part. / Merge with the document “fulminata_maximus_specs”.
A2	12/26/07	Céline Buret	Update HAL CL -> HAL HLE.
A3	02/04/08	Céline Buret	Add the HAL Leon.

Readers
Etienne Chevreau	SPIDCOM Technologies
Céline Buret	SPIDCOM Technologies

Distribution
Etienne Chevreau	SPIDCOM Technologies

END