Cleopatre

Manager daemon

2010/09/15
rev. A5

© 2009 SPiDCOM Technologies, ALL RIGHTS RESERVED

SPC, SPR, SCR, SVR are trademarks of SPiDCOM Technologies.

All other products or services mentioned herein may be trademarks of their respective owners.

Notice: No part of this publication may be reproduced or transmitted in any form or by any means, electronic or mechanical, including photocopying and recording, or stored in a database or retrieval system for any purpose without the express written permission of SPiDCOM Technologies.

SPiDCOM Technologies reserves the right to make changes to this specification at any time without notice and assumes no responsibility for its use. This specification contains the most current information available at the time of publication.
# Introduction
## Forewords
This document contains Cleopatre Manager daemon. Its goals are :

## References
REF1 : Cleopatre MME specification
File : cleopatre_mme_specs.odt
revision A13

## Acronyms
AFE	Analog Front End
GPIO	General Purpose Input/Ouput
NVRAM	Non Volatile RAM
PHY	PHYsical layer device
MME	Management MEssage
EOC	Ethernet Over Cable

# Managerd specification
## Presentation
Managerd is a user level daemon which is in charge of managing all MME not processed by the PLC daemon nor the Cesar firmware.
It is listening all MME packets coming from the br0 bridge and process them only if they fit the list of its MME.
Managerd is mandatory inside the Cleopatre architecture to manage all data in relation with system, like configuration or information data, and to get them from or store them inside the SDRAM and flash memory.
Indeed, as PLC driver and Cesar are not able to access to filesystems, only manager daemon and plc daemon are able to manage these data.
## Architecture

br0
eth0
plc0

IPMbox
(H1 interface)
MME
EOC_MME
plc
driver

Cleopatre
kernel
plc
daemon
VS_MME
spidlib

config
(files /
NVRAM)

MME

plc interface

DRV_MME
manager
daemon

MME

## Parameters

## Communication with PLC daemon
### Introduction
GPIO-s and LED-s are managed by manager daemon. How to communicate with manager daemon from an external daemon or application to control a GPIO or a LED?
Moreover, as shown on the architecture, manager daemon has only 2 links: one with “br0” network interface, and the other one with Libspid. How to communicate with other processes respecting these constraints?
To do this, a signal mechanism is used; It is detailed in following paragraphs.

### Management of Simple Connect button
When Simple Connect button is pressed by user, information has to be propagated to Cesar. To do this, manager daemon has to inform PLC daemon, which can send MME-s to Cesar via PLC driver.

When SC button is pressed, manager daemon has to update hpav.info file with following information:
SC_BUTTON = yes
After having updated this file, manager daemon has to signal it to other processes by calling libspid_system_file_update_warn() function, which sends a SIGHUP signal to PLC daemon (which has preliminary registered).

Once SC button is released, manager daemon has to reset SC button status of hpav.info file:
SC_BUTTON = no
And to inform other processes about this file modification.

### Management of LED-s
To control LED-s, PLC daemon sets some information [TBD] in hpav.info file.
To be noticed by SIGHUP signal when hpav.info file is modified by another process, manager daemon has to be preliminary registered on hpav.info file by calling libspid_system_file_update_register() function.

### Libspid concerned functions
Libspid provides 4 functions relative to signal management. They are listed below.

libspid_error_t libspid_system_file_update_register (pid_t rx_pid, const char *filename, const libspid_signal_handler_t callback);

libspid_error_t libspid_system_file_update_unregister (pid_t rx_pid, const char *filename);

libspid_error_t libspid_system_file_update_is_registered (pid_t rx_pid, const char *filename, libspid_boolean_t *is_registered);

libspid_error_t libspid_system_file_update_warn (pid_t tx_pid, const char *filename);

## Vendor specific MMEs
### VS_GET_VERSION
Provide the current and alternate image version. Field to get are :
- current index : the index of current running image
  - get current image mtd name with spidlib_image_get_desc()
  - get image #0 mtd name with spidlib_image_des()
  - compare to retrieve the current index (0 or 1)
- current application version
  - get current image version name with spidlib_image_get_desc()
  - version is image_desc->version
- current av stack version : same as application version
- alternate applicative version
  - get alternate image version name with spidlib_image_get_desc()
  - version is image_desc->version
- alternate av stack : same as alternate applicative version

### VS_RESET
Reboot the modem.
- answer to the MME request (with the CNF MME)
- call spidlib_system_reboot()

### VS_GET_NVRAM
Here, NVRAM means the whole flash sector used for storing non volatile informations (64KB length).
- open MTD_NAME_NVRAM (/dev/mtd1)
- seek block_index * 1024 bytes
- read 1024 bytes and return them

### VS_GET_LOOPBACK

### VS_SET_LOOPBACK

### VS_GET_TONEMASK
Manufacturing set tonemask, for frequency carriers.
access : RO
location : nvram->tonemask field

### VS_GET_ETH_PHY
Provided into /proc/net/eth/phy

### VS_ETH_STATS
Get or clear Ethernet interface statistics.
All stats can be retrieved from /proc/net/dev file.
To clear stats, an extension of ethtool / eth driver must be added.

### VS_GET_STATUS
Cesar current status retrieved by plcd.
- status : hpav.info<STATUS>
- cco : hpav.info<CCO>
- preferred CCO : hpav.conf<CCO_PREFERRED>
- backup CCO : hpav.info<BACKUP_CCO>
- proxy CCO : hpav.info<CCO>
- simple connect : hpav.info<SC>

### EOC specific MMEs
#### Presentation
All dedicated EoC MME are implemented inside the eoc.c module.
bridge_processing() from the module bridge.c has to be updated.
Inside this function, the incoming MME type will be analyzed. If the type is VS_EOC_* according functions from module eoc.c will be called in order to fetch data needed for preparing confirmation MME .
Confirmation MME will be sent by already existing function bridge_send from module bridge.c.

#### VS_EOC_GET_DEVICE_INFO
It gets device informations: model number, software version, downstream attenuation and port amount.
The functions which implements handling of this MME will be stored in module eoc.c.

Model number and port amount are stored in NVRAM. In order to get this data, libspid function libspid_system_get_nvram will be called.
To get software version, libspid function libspid_image_get_desc will be called.
Downstream attenuation will be fetched by sending according MME between Cleopatre and Cesar on STA side.

#### VS_EOC_AUTOCONF_START
This MME shall trigger the start of slave auto-configuration procedure.
Function vs_mme_eoc_autoconf_start will first check if the protocol matches and then it will try to lock the auto-configuration. If lock is successful, sent CNF will enable configuration file transfer. Otherwise (i.e. if another configuration procedure is in progress), auto-configuration start will fail. Protocol version has to match as well.

#### VS_EOC_AUTOCONF_TRANSFER
vs_mme_eoc_autoconf_transfer function that shall handle this MME will be used to store incoming configuration into temporary file on slave side. Several VS_EOC_AUTOCONF_TRANSFER MMEs can be used to transfer the new configuration.

#### VS_EOC_AUTOCONF_END
This MME is used to signal the end of the configuration process and it shall be handled by vs_mme_eoc_autoconf_end function. Assembled configuration package will be checked for MD5 sum, unpacked and optional /etc/init.d/S88slave file will be executed.

## Manufacturer specific MMEs
### MS_UPDATE_*

### MS_SET_NVRAM
Write the NVRAM flash sector.
- if index = 0, first erase the sector, then write the 1024 bytes block.
- if index != 0, write the block to index * 1024 address.

### MS_SET_IMAGE
Change the current firmware image to image #0 or #1.
use spidlib_image_select()

### MS_SET_TONEMASK
Set a new tonemask inside the NVRAM.
- get the NVRAM with spidlib_system_get_nvram()
- change the tonemask into the retrieved NVRAM structure.
- erase the NVRAM sector and write the new NVRAM structure
- reboot the modem with spidlib_system_reboot()

# History

Revision	Date	Comments
A0	2009/08/25	JLe : creation
A1	2009/11/23	ZMc: update with EOC specific MME
A2	2009/12/02	ZMc: fixed typo's, added small additional information
A3	2009/12/03	ZMc: accepted changes from JLe
A4	2010/09/06	AS: auto-configuration MMEs
A5	2010/09/15	CBu : / - add SIGHUP transmission and reception / - add SC button and LED management